## Slide 1: AI-Based Smart Streetlight Energy Optimization
Capstone Project • Second-Year EEE
Machine Learning + Sensor-Based Lighting

## Slide 2: Problem Statement
Conventional streetlights can use full power when full brightness is not needed.
The project uses ambient-light and motion inputs to select a suitable lighting mode.
Goal: reduce unnecessary energy use while keeping lighting responsive to movement.

## Slide 3: Objectives
Collect or simulate timestamp, ambient-light and motion data.
Preprocess data and explore sensor patterns.
Train and evaluate a classification model.
Predict OFF, DIM or HIGH lighting mode.
Estimate energy use and display results on a dashboard.

## Slide 4: System Block Diagram
LDR ambient-light sensor + PIR motion sensor + time input
↓ Data logging and preprocessing
↓ Machine-learning classifier (Random Forest)
↓ Lighting decision: OFF / DIM / HIGH
↓ LED driver → low-voltage LED streetlight

## Slide 5: Hardware and Software
Software: Python, Pandas, NumPy, scikit-learn, Matplotlib, Streamlit.
Optional hardware: ESP32/Arduino, LDR module, PIR sensor, low-voltage LED and driver.
The supplied prototype is a software simulation; hardware is an optional extension.

## Slide 6: Dataset and Features
Inputs: hour of day, ambient light in lux, motion detected (0 or 1).
Target: lighting mode (OFF, DIM or HIGH).
Dataset included: 1,200 simulated records with 5-minute timestamps.
Labels use a simple rule so the workflow is reproducible.

## Slide 7: Machine-Learning Method
Split dataset into training and test sets (80% / 20%).
Train a Random Forest classifier.
Evaluate with accuracy, precision, recall, F1-score and confusion matrix.
Important limitation: synthetic labels cannot establish real-world accuracy.

## Slide 8: Control Policy
OFF: ambient light is sufficient (≥ 250 lux).
HIGH: dark conditions and motion detected.
DIM: dark conditions and no motion detected.
Demonstration brightness levels: OFF 0%, DIM 35%, HIGH 100%.

## Slide 9: Energy Calculation
Assumption: one 30 W LED operates for 12 hours each night.
Baseline: 30 W × 12 h ÷ 1000 = 0.360 kWh/night.
Smart example: 25% at 30 W and 75% at 12 W = 0.198 kWh/night.
Estimated saving = (0.360 − 0.198) ÷ 0.360 × 100 = 45%.
This is an assumption-based estimate, not a measured result.

## Slide 10: Dashboard and Expected Output
Interactive inputs: hour, ambient light and motion status.
Outputs: predicted lighting mode, brightness and estimated power.
Visuals: mode counts, model metrics and confusion matrix.
Energy comparison: baseline, smart policy and estimated savings.

## Slide 11: Safety and Limitations
Data are simulated; collect real readings before claiming field performance.
Use only a correctly rated low-voltage LED driver in a student prototype.
Never connect an LED directly to an ESP32/Arduino GPIO.
Do not work with mains voltage; have an instructor check the circuit.

## Slide 12: Conclusion and Future Scope
The project demonstrates an end-to-end ML workflow for adaptive lighting.
Future work: collect real data, test under varied weather and traffic, and calibrate sensors.
A supervised low-voltage prototype can validate the controller and energy estimates.

## Slide 13: Viva Questions
What does an LDR measure? — Ambient light intensity.
What does a PIR sensor detect? — Motion-related changes in infrared radiation.
Why Random Forest? — It combines decision trees and models non-linear patterns.
How is energy calculated? — Power (W) × time (h) ÷ 1000 = kWh.
Is 45% saving measured? — No, it is based on stated assumptions.